## Slide 1
INSIZE
INSIZE INDIA LLP
V.1 05.2026
www.insize.in
MEASUREMENT SOLUTION PROVIDER
DATA
TRANSMISSION
AND MANAGEMENT
Quality Innovation Service Value

## Slide 2
About us
is our standard quality, made in China
is our premium quality, made in Europe
INSIZE - Founded in 1995, is a dedicated supplier of measuring instruments. To enable us to serve the world-wide market, we are setting up an INSIZE distribution network on a global basis. INSIZE headquarter is located in China. We have branch companies in Canada, USA, Mexico, Brazil, India, Turkey, Malaysia, Thailand, Vietnam, UAE, Spain, France, Italy, UK, Poland, Czech Republic, Romania, Slovenia, Australia and distributors in over 120 countries. We ensure that wherever you are, our INSIZE products have service and support that are within hands reach. Our dedication to Quality, Innovation, Service and Value has created a worldwide demand for the INSIZE products.

## Slide 3
Supports multiple measurement tools for real-time data collection. One-click transfer of measurement data to Excel, measurement software or mobile APP after measurement. This process is efficient and accurate, and facilitates data management and sharing to improve productivity.
Data Transmission And Management
— Improve productivity
Transfer To Excel
Transfer To Data Management Software
Transfer To Phone APP

## Slide 4
Advantages of Data Transmission (P1)
Traditional Measurement
Communication Transfer Data
VS
Traditional measurement is manual recording is inefficient, you need to measure and record at the same time; sometimes you need two operators for operation, one to measure and the other to record.
Data can be transmitted directly to a computer /phone through wired or wireless data transmission, improving efficiency.
Timeliness
Traditional measurements are made by manually recording data to a paper file or manually entering it into a computer, which inevitably results in recording errors.
The direct transmission of measurement data to the computer, eliminating human error and ensuring that the data is true.
Validity
Traditional measurements use paper forms, which are difficult to save , circulate and trace at a later stage.
Compared to paper forms, electronic forms of data transmission are more convenient for storage, transferring between each other and later reference.
Paperless

## Slide 5
Advantages of Data Management (P2)
OEMs can conduct random inspections to verify if results align with those from suppliers and ensure full production traceability.
Data Management
SPC analysis
Manages measurement data for
easy traceability and review.
Analyzes measurement data to identify production inefficiencies and optimize workflows.
defect rate
capability run chart
Reports
Provides inspection reports upon production completion, enhancing quality credibility.
Real-time monitoring of process quality to address risks promptly.
Panel
01
OEMs
can be connected with PDM,
ERP, MES and other systems
Data Acquisition
Work
Station
1
Work
Station
2
Work
Station
3
Supplier
3
Supplier
2
Supplier
1
file parsing
Supports multiple data collection methods,
compatible with mainstream measuring tools
data transmission
screen capture

## Slide 6
Agenda
01
Wireless Data Transmission
02
Wired Data Transmission
03
Measurement Data Management and Analysis Software
04
Inspection Table

## Slide 7
01
Wireless Data
Transmission

## Slide 8
Wireless Data Transmission System
External Transmitter
Connecting to
indicator
Transmitter
Connecting to
caliper
Transmitter
Connecting to
micrometer
Transmitter
Measuring tool connects to a transmitter to send data , and receiver received data
Trigger the transmit button of transmitter to wirelessly transfer measurement data to a computer /phone
Transmission distance : 15m (unobstructed, no electromagnetic interference)
Customizable AES128 data encryption to enhance data security
Connects to PC/Phone/Tablet
transmit button
transmit button
transmit button

## Slide 9
Wireless Data Transmission System
Built-in Wireless
The built-in wireless measuring tool sends data, and receiver received data
Transmission distance 10m(unobstructed, no electromagnetic interference)
Trigger the transmit button of measuring tool to wirelessly transfer data to the PC/phone
signal light
transmit button
transmit button
signal light
transmit button
signal light
transmit
button
signal light

## Slide 10
Receiver
The data entry jump direction can be switched according to needs, either downwards or to the right. Custom output formats can also be tailored.
Single Channel Receiver
(Keyboard Signals)
can be connected to 1 transmitter
Multichannel Receiver
(Keyboard Signals)
can be connected to 6 transmitters
Multichannel Receiver
(virtual com port)
can be connected to 16 transmitters, each has an unique identification code
For computers with windows system.
Outputs serial port signals, to be used with software.
For computers and mobile phone with Windows, Android, and iOS system
Recognized as HID keyboard device, the transmitted data is recognized by computers or mobile phones as keyboard input data and press enter key, such as 12.34 ↙
No need to install drivers and softwares.
Data can be transmitted to excel, word, txt etc.
For any softwares which can receive keyboard signal.
The receiver connects to the transmitter or built-in wireless measuring tool, receiving data wirelessly.

## Slide 11
Excel Directional Input Software
(7315-2 Receiver Included)
The readings of measuring tools can be transmitted to the designated area of excel, which facilitates data management and improves efficiency.

## Slide 12
Wireless Data Transmission System of Digital
Indicators (Remote control) 7213
Transmitter
Transmitter
Transmitter
Transmitter
Transmitter
Transmitter
receiver
transmit button
The button on receiver is pressed once, the readings of all digital indicators are transmitted
channel 1
channel 2
channel 3
channel 4
channel 5
channel 6
Digital indicator connects to a transmitter to send data, and receiver received data
Trigger the transmit button of receiver to transfer data from multiple digital indicators to computer/phone

## Slide 13
Transmission distance: 15m (external transmitter), 10m (built-in transmitter).
Stable data transfer within the effective range, no data loss or errors.
Point-to-point transfer between measuring tools and collection terminal, with memory after
pairing—no need to reconnect.
Data can be transferred normally after rebooting the computer/phone, no connection required.
When transferring data, data with ID number is for easy identification of the source.
Wireless Data Transmission 7315 -- Advantages

## Slide 14
Wireless Data Transmission VS.
Competitor Brands Advantages
Our receivers feature multiple interfaces (USB, Type C, Micro USB, and Lightning), compatible with various system terminals such as computers, tablets, or phones
running Windows, Android, or iOS.
01
High Compatibility‌
Comprehensive Coverage‌
02
Three product categories: built-in wireless transmitters, external wireless
transmitters, and all-in-one transmitters. our wireless data transmission capability
comprehensively covers commonly used measuring tools and instruments.
04
User-Friendly Operation‌
Simplified device pairing, unpairing, and data transfer processes for effortless setup.
05
Persistent Binding Mechanism‌
Single-pairing ensures continuous data transmission—no re-pairing required
when replacing terminals, instruments, or batteries.
Operates for over ‌400,000 transmissions‌ on a single CR2032 battery.
06
Ultra-Low Power Consumption‌
Data Format
07
Supports multiple data fomats: e.g., Value + Enter, Value + TAB, ID number + Value
+ Enter, etc.
Data Security‌
Optional ‌AES128 encryption‌ for critical data protection.
08
09
Deep Customization‌
Provides bespoke data transmission solutions tailored to client specifications.
10
Advanced Analytics Capabilities‌
Mature supporting software collects, aggregates, and analyzes measurement data, enabling streamlined, intelligent, and visualized data management.
Diverse Communication Protocols‌
Supports both ‌emulated keyboard signals‌ and ‌serial port signals‌ to accommodate
varied industrial scenarios.
03

## Slide 15
02
Wired Data Transmission

## Slide 16
连接使用
press red button
to transmit data
Connecting to caliper
press black button to transmit data
can also press the foot
switch to transmit data (optional)
Recognized as HlD keyboard device by computer, no need to install drivers and softwares.
Data can be transmitted to Excel, Word, txt and other files (press transmit button, which is recognized by the computer as keyboard input data and press enter key, such as 12.34↙).
For any softwares which can receive keyboard signal.
Cursor movement direction after data input can be switched (down/right).
Supports output of ID numbers if needed, e.g., 2023032265 12.34.
Wired Data Transmission (keyboard Signals)
7302
Measuring tool connects to the data output cable, and trigger the transmit button to wired transfer data to a computer/tablet
Connecting to digital
indicator/micrometer

## Slide 17
Wired Data Transmission
(Text Format, Virtual Com Port) 7305
press red button
to transmit data
can also press the foot
switch to transmit data (optional)
Connecting to digital indicator
Measuring tool connects to the data output cable, and trigger the transmit button to wired transfer data to a computer
Output serial signals to transfer data to serial communication software.
Supports output of ID numbers if needed, can designated area to input data from different measuring tool, e.g., 2023032265 12.34.
Connecting to digital
indicator/micrometer/caliper

## Slide 18
485 Data Output Cables 7215
Connect the measuring instrument to the data cable, and connect the data cable to the PLC to enable automated control of the measurement data.
Modbus-RTU Protocol
• Configurable baud rates (9600, 19200, 38400)
Can set communication address
Application
PLC Control Panel
Automated Control System
7215-40M Data Output Cable(RS485)

## Slide 19
Wired Data Transmission Comparison
Adapted Terminals
Data Collection Methods
Transmission Performance
Communication
type
7305 Series (Serial Signal)
keyboard format (suitable for any software or APP
which can receive keyboard input values)
text format, virtual com port (a. connection to software that recognizes different channels and IDs
according to serial communication protocols and defines data entry area
for different measurement tools; b. can also use the included software (included in the 7210-2
interface box) to transfer measurement data from multiple measuring
tools to the designated area in Excel for easy data management)
Wired transmission directly transfers data through physical connections, offering strong anti-interference capability,
stable signals, high speed, and good security. It supports high-bandwidth data transmission.
Computers or tablets with Windows, Android, or iOS systems (USB interface supported)
Computers or tablets with Windows system
(USB or RS232 interfaces supported)
Single key press transmission or
command transmission or
real-time continuous transmission
Single key press transmission
PK
7302 Series(Keyboard Signal)
7215 Series (485)
Modbus-RTU protocols
(Connecting a PLC for automated data control)
PLC
(Terminal block)
Command Transmission

## Slide 20
GO And NO-GO Signal Output Cable 7132 (P1)
GO and NO-GO signal output cable
gauge
workpiece
Connects gauge with signal output cables, automatically judgment and wired transmitting the judgment result OK or NG to the computer.
output NG (out of upper tolerance)
output NG (out of lower tolerance)
output OK (within tolerance)
Suitable for metal workpieces

## Slide 21
If the No-Go end of gage can be inserted into the workpiece, it is out of upper tolerance and output NG
If the Go end of gage cannot be inserted into the workpiece, it is out of lower tolerance and output NG
If the Go end of gage can be inserted into the workpiece, but the No-Go end of gage cannot be inserted into the workpiece, it is within tolerance and output OK
Output cable with two sensors
GO And NO-GO Signal Output Cable 7132 (P2)

## Slide 22
GO And NO-GO Signal Output Cable 7132 (P3)
If the workpiece cannot enter into the upper tolerance section, it is out of upper tolerance and output NG
If the workpiece can enter into the lower tolerance section, it is out of lower tolerance and output NG
If the workpiece can enter into the upper tolerance section, but the workpiece cannot enter into the lower tolerance section, it is within tolerance and output OK
Output cable with three sensors

## Slide 23
OK/NG Input switch 7327
Transmit the OK/NG results to the computer via a wired switch.
hand switch
foot switch
Output NG for appearance defects
Output OK for appearance qualified

## Slide 24
Adaptable to multiple acquisition terminals
a. Computers or tablets with Windows, Android or iOS systems b. PLC
Adapted Terminals
01
Communication
types
02
Multiple data communication types to meet various production application scenarios:
a. (Simulated keyboard signal) Directly transfer data to Excel reports or customer measurement software, MES, or ERP systems
b. (Output serial port signal ) Interface with serial communication software, or transfer measurement data from multiple gauges to the
designated area of Excel for easier data management
c. (485) Can be connected to a PLC to enable automated control of measurement data
Supports multiple data formats: e.g., Value + Enter, Value + TAB, ID number + Value + Enter, etc.
Data Format
03
Output the judgment result OK or NG
Special Data
Types
04
Wired Data Transmission VS.
Competitor Brands Advantages

## Slide 25
03
Measurement Data Management
and Analysis Software

## Slide 26
Measurement Data Management and Analysis Software (Basic Version)-- 7349 （P1）
Can be connected with
PDM,ERP, MES and other systems
Measuring tools Management
Automatically collects measurement data from measuring tools (e.g., digital calipers, micrometers, digital indicator , …), analyzes and manages the measurement data to improve production quality.
Software modules: Measuring tools management, inspection plan, data acquisition, data management, SPC analysis and quality reports
Make inspection plan
Quality report
Data acquisition
SPC analysis
Data management

## Slide 27
Support multiple data acquisition methods:
Manual input: data input with keyboard
Data transfer: data collection with data output cable
Manual Input
Data Transmission
Drawing-guided measurement, and acquisition
data of measuring tools
SPC Analysis: average, min value, max value, range, Cp, Cpk, variation, sigma, counts of OK/NG.
Quality Analysis Control Charts: Pie chart, X chart, Xbar-R chart, Xbar-S chart, I-MR chart and Run chart.
Query measurement data (red display for out-of-tolerance) and result status (OK/NG, Rework, UpMax/LowMin).
Manage basic information and calibration dates of measuring tools.
Generate quality reports with control plan information, SPC parameters, and measurement data, can export Excel.
Measurement Data Management and Analysis Software (Basic Version)-- 7349 （P2）
Data acquisition
Measuring tool management
Data Management
SPC analysis
Quality report

## Slide 28
Measurement Data Management and Analysis
Software -- 7317 （P1）
Automatically collects measurement data from measuring tools (e.g., digital calipers, micrometers, digital indicator, …)
Automatically collects measurement data from file of CMM, Vision measuring tools, and other measurement tools.
Analyze and manage measurement data to improve production quality.
Software modules: Inspection plan, data acquisition, data management, SPC analysis and panel，quality reports.
Make inspection plan
Management of inspection plan
Data acquisition
SPC analysis
Panel
Report
Can Be Connected With PDM,
ERP, MES And Other Systems

## Slide 29
Supports multiple data acquisition methods:
Manual input
Data transmission
File parsing
Screen capture
Quality reports increase quality credibility, reduce acceptance workload, and ensure traceable quality control.
Measurement data analysis helps identify engineering limitations and optimize workflows.
Quality control personnel can monitor real-time quality status for each process and address risks promptly.
Guiding the operator to measure follow the inspection plan to reduce human errors such as missed or incorrect inspections.
Manual input
File parsing
Screen capture
Data transmission
Measurement Data Management and Analysis
Software-- 7317 （P2）
Data acquisition
Guided measurement
Real Time Monitoring
SPC Analysis
Reports

## Slide 30
Data Management APP
Measuring tools connects to the mobile APP by Bluetooth for real-time data collection
Displays synchronized data with automatic judgment (red display for out-of-tolerance)
Data trend charts help quickly identify abnormal fluctuations
Export data as PDF, JPEG, or Excel files
Transmission distance: 10 meters

## Slide 31
04
Inspection Table

## Slide 32
The small and lightweight station is easy to move, and equipped with a 23.6-inch touchscreen computer (i7 CPU&Windows system)
CAN BE
CUSTOMILZED
L×W×H : 650x600x1617mm
storage drawer
(customizable cavity)
touchscreen computer
Digital Measurement Station -- 7906-06
scan window(scan barcode
or QR code of workpieces)
measurement data management
and analysis software
receiver
data output cable
foot switch
(transmission data)
Application

## Slide 33
Inspection Table
Customers can choose the suitable inspection table based on different measurement applications.
7901
7911
7923

## Slide 34
SPC Inspection Station Case
Bore Plug Gage 4653-B34J8
(For measuring Ø34J8+0.024/-0.015)
Dial snap Gage 2186-125/275
(For measuring Ø105n6+0.045/+0.023/ Ø270h7 0/-0.052)
Using the 7315 wireless transmission system, measurement data is directly transferred to the 7317 software.
Ring Outer Diameter Plug Gage 4659-D250g6
(For measuring Ø250g6-0.015/-0.044)
receiver
transmitter
1. Customer needs to quickly measure the inner and outer diameters of automotive differentials.
2. Measuring tools were selected for quick on-site measurements and to minimize human errors: 4653 precision
Bore plug gauge, 2186 quick dial snap gauge, and 4659 ring type inner/outer diameter plug gauge.
3. The 7315 wireless data transmission system was selected, and transmit data to the 7317 software.

## Slide 35
THANKS !
Quality Innovation Service Value